## Slide 1
Lecture 2 4CS015: Digital Electronics
Prepared by: Uttam Acharya
1

## Slide 2
1. Lecture 2 Coverage
2
Boolean logic and logic gates
Truth table
Boolean algebra laws
Combinational logic

## Slide 3
2. Boolean Logic
3
George Boole (1815-1864)
  “An Investigation into the Laws of Thought”
  Defined an algebra for solving logical problems
  Limited to dealing with facts True or False
  Now known as Boolean Algebra

## Slide 4
3. Basic Logic Definitions
4
In a Logic System a variable can have one of two possible states.
Single capital letters are used to represent variables.
The bits 1 and 0 are also used as constants.
TRUE | ON | CLOSED | ‘1’ | Yes | 5v
FALSE | OFF | OPEN | ‘0’ | No | 1v

## Slide 5
4. Logic States
5
If a switch is closed:
  The light will be ON.
  This can represent Logic TRUE.
If a switch is open:
  The light will be OFF.
  This can represent Logic FALSE.
The switch is a Logic variable.

## Slide 6
5.Boolean Basics: operators
6
Boole defined three basic operations that could be used with these Boolean variables.
  AND
  OR
  NOT
All logical expressions can be built from these three.

## Slide 7
5.Boolean Basics: operators
Logical AND
Logical OR
Logical NOT
A B
F
A B
F
A
7
F

## Slide 8
5.1 Logical 'AND'
How can we switch the light on?
Light
8
Battery
Switch A
Switch B

## Slide 9
5.1 Logical 'AND'
Boolean Expression:
F = A AND B or F= A∙B
Gate Diagram:
Truth Table:
A B
9
F
Input A | Input B | Output F
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1

## Slide 10
5.1.1 The AND relationship.
10
Boolean representation .
If F,A and B are Boolean variables.
Then the expression F = A∙B means
  F is only true when A AND B are both true.
As A is capable of being 1 or 0 and B is capable of being 1 or 0 there are 4 possible states. 00, 01, 10 or 11

## Slide 11
5.2 Logical 'OR'
Battery
Switch A
Switch B
Light
How can we switch on the light?
11

## Slide 12
5.2 Logical 'OR'
Boolean Expression:
F = A OR B
Gate Diagram:
alternatively F =A+B
Truth Table:
13
Input A | Input B | Output F
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1

## Slide 13
5.2.1 The OR relationship.
13
Boolean representation +
If F,A and B are Boolean variables.
Then the expression F = A+B means
  F is only true when A OR B, OR both, are true.
As A is capable of being 1 or 0 and B is capable of being 1 or 0 there are 4 possible states. 00, 01, 10 or 11

## Slide 14
5.3 Logical 'NOT'
How can we switch the light off?
Battery
14
Switch A
Light

## Slide 15
5.3 Logical 'NOT'
oBoolean Expression:
o F = NOT A or F=!A or F=A
oGate Diagram:
oTruth Table:
A
F
Input A | Output F
0 | 1
1 | 0
The circle means NOT
15

## Slide 16
5.3.1 Boolean NOT
The NOT relationship reverses the value.
NOT True is False etc…
The Symbol( ) used is usually a bar above the variable or expression to be reversed
E.g if A= true then A = false
In some circumstances we use !
E.g. if B = true !B = false (easier to type)
16

## Slide 17
6. Relationship Between Integrated Circuits and Logic Gates
17

## Slide 18
7. Other Logic Gates
18
To make life a little easier the basic logical functions are expanded to include:
NAND.
  This is an AND with a NOT output.
NOR.
  This is an OR with a NOT output.
XOR.
  This is the Exclusive OR function.

## Slide 19
7.1 NAND
Boolean Expression:
F = NOT(A AND B) or F = A∙B
Gate Diagram:
o Truth Table:
A B
F
Input A | Input B | Output F
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
19

## Slide 20
7.2 NOR
Boolean Expression:
F = NOT(A OR B) or F = A+B
Gate Diagram:
Truth Table:
A B
F
Input A | Input B | Output F
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
20

## Slide 21
7.3XOR
Boolean Expression:
F = A XOR B or F = A⊕B
Gate Diagram:
Truth Table:
A B
21
F
Input A | Input B | Output F
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 22
8. Boolean Algebra Laws :
The operations +, and ͞ consequently satisfy the basic laws 1, 2 and 3 of Boolean algebra. That is:
1.
A + B  B + A
A  B  B  A Commutative Laws
2.
(A + B) + C  A + (B + C)
(A  B)  C  A  (B  C) Associative Laws
`
3. A  (B + C)  (A  B) + (A  C)
A + (B  C)  (A + B)  (A + C)
Distributive Laws
22

## Slide 23
8.Another Boolean Algebra (Contd.):
23
Identity Law Negation Law
A + 0 = A low = high
A . 1 = A ( 0 = 1 )
Idempotent Law
A + A = A
A . A = A
Complement Law
A . A = 0
A + A = 1
Double Negation Law
A = A
Domination Law
A + high = high A . low = low
(A + 1 = 1) A . 0 =0
Absorption Law
A + (A .B) = A
A . (A + B) = A

## Slide 24
9. DeMorgan’s Law 1
24
A+B = A .B

## Slide 25
10. DeMorgan’s Law 2
25
A.B = A+B

## Slide 26
11. Question1 : NAND and NOR gates are called universal gates, why?
26

## Slide 27
12. Precedence of operators
27
As with normal mathematics when working out the value of a function it is very important to do it in the right order.
NOT AND OR
Parenthesis (brackets) override in the normal way.
When a bar goes above more than 1 symbol it becomes a bracket that reverses.

## Slide 28
Example 6. F= A+B.C
Example 7. F= A .B + (C +A) .D+E+G
Example 1. F= A.B.C
Example 2. F= C.A.B
Where
A=1 B=1 C=0 D=1 E=0 G=1
Evaluate these examples
Example 3. F= A+B+C
Example 4. F= A.B+C
Example 5. F= A+B.C
0
0
28
1
1
1
0
1

## Slide 29
13 Truth table

## Slide 30
14.Circuit Design:
This circuit uses three gates (two NOT gates and an AND gate)
31

## Slide 31
The main thing to remember is that combinations of gates implement Boolean functions.
The circuit below implements the Boolean function:
We simplify our Boolean expressions so that we can create simpler circuits.
31
14.1 .Digital component

## Slide 32
We have designed a circuit that implements the Boolean function:
This circuit is an example of a combinational logic
circuit.
Combinational logic circuits produce a specified output (almost) at the instant when input values are applied.
  In a later section, we will explore circuits where this is not
the case.
32
14.1 .Digital component​

## Slide 33
14.2 Simple Combinatorial Logic
(Example 1)
Circuit after Simplification
33

## Slide 34
14.3 Example 2:
34

## Slide 35
14.4 Example 3:
35
Simplify:
X = (A.B.C) +(A.B'.C) +(A'.B.C)

## Slide 36
14.5 Exercises ……
Simplify and construct the logic circuit:
A’.B’ + (A.B)’
(A + B).(A + B) + A.(A + B’)
(A.B’.C’ + A’.B’.C+A.B.C+A’.B.C’)
36

## Slide 37
15. Summary
37
We have looked at the basic logic gates:
  Identifying OR, AND, NOT, NAND, NOR and XOR.
We have seen that gates can be joined together to form Combinatorial Logic.

## Slide 38
38